## Slide 1: ROBOTICS COMPETITION
Rebecca, Josh, Aarnik, Ryun, Shreyas

## Slide 2: Functions
follow_segment(): This function, causes the 3pi to follow a segment of the maze until it detects an intersection, a dead end, or the finish
turn(unsigned char dir): Code to perform various types of turns according to the parameter dir, which should be 'L' (left), 'R' (right), 'S' (straight), or 'B' (back). The delays here had to be calibrated for the 3pi's motors.
select_turn(unsigned char found_left, unsigned char found_straight, unsigned char found_right): This function decides which way to turn during the learning phase of maze solving. It uses the variables found_left, found_straight, and found_right, which indicate whether there is an exit in each of the three directions, applying the "left hand on the wall" strategy.
simplify_path(): Path simplification. The strategy is that whenever we encounter a sequence xBx, we can simplify it by cutting out the dead end. For example, LBL -> S, because a single S bypasses the dead end represented by LBL.

## Slide 3: Algorithms
Left Hand on the Wall: It’s like keeping your left hand on the wall at all times. You’ll turn left whenever possible and only turn right at an intersection if there is no other exit.
Proportional Integral Derivative Control: Uses continuous functions to compute the motor speeds, so that the jerkiness of the previous example can be replaced by a smooth response. Does this in 3 phases. The proportional value is approximately proportional to your robot’s position with respect to the line. The integral value records the history of your robot’s motion. The derivative is the rate of change of the proportional value.

## Slide 4: Libraries
<Pololu3pi.h> : Used to interface all the sensors and read off their values.

## Slide 5: THANK YOU!!